## Slide 1: Earthquake Contingency Planning in Nepal to Save life and property

## Slide 2
Overview
2015 Gorkha earthquake was worst in 90 years
8970 fatalities, 22,309 injuries, 3.5 million displaced
Not as large as had been expected – Mw 8.5+ earthquake anticipated with 100,000+ fatalities (Dixit et al 2014; Bilham et al. 2001, Wyss, 2005)
Scope of this planning:
  To forecast absolute impacts to residential buildings:
    Fatalities
    Injuries
    Building Collapse
    Displaced population
  Focus on large EQs requiring International response
    M7.0 – M8.6
  Results at all Administrative levels
Rockfall damage in Kodari

## Slide 3
Chart: Complete Damage
| 0 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1000000000000001 | 1.1499999999999999 | 1.2 | 1.25 | 1.3 | 1.35 | 1.4 | 1.45 | 1.5 | 1.55 | 1.6 | 1.65 | 1.7 | 1.75 | 1.8 | 1.85 | 1.9 | 1.95 | 2
BIC_flex_floor | 0 | 4.7293e-11 | 1.3627e-05 | 0.0021082 | 0.027735 | 0.11877 | 0.28048 | 0.47037 | 0.64241 | 0.77408 | 0.8641 | 0.92109 | 0.95531 | 0.97512 | 0.9863 | 0.99251 | 0.99592 | 0.99778 | 0.99879 | 0.99934 | 0.99964 | 0.9998 | 0.99989 | 0.99994 | 0.99997 | 0.99998 | 0.99999 | 0.99999 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
BIC_rigid_floor | 0 | 4.7296e-14 | 1.7112e-07 | 9.8003e-05 | 0.0029896 | 0.023158 | 0.08465 | 0.19713 | 0.34485 | 0.5 | 0.63951 | 0.75182 | 0.83527 | 0.89371 | 0.9329 | 0.95833 | 0.97443 | 0.98445 | 0.9906 | 0.99434 | 0.9966 | 0.99796 | 0.99878 | 0.99927 | 0.99956 | 0.99973 | 0.99984 | 0.9999 | 0.99994 | 0.99996 | 0.99998 | 0.99999 | 0.99999 | 0.99999 | 1 | 1 | 1 | 1 | 1 | 1 | 1
BIM / Adobe | 0 | 2.1834e-05 | 0.013776 | 0.13527 | 0.37446 | 0.61268 | 0.78282 | 0.88505 | 0.94103 | 0.97019 | 0.98499 | 0.99243 | 0.99615 | 0.99803 | 0.99898 | 0.99947 | 0.99972 | 0.99985 | 0.99992 | 0.99995 | 0.99997 | 0.99999 | 0.99999 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SIM | 0 | 0.00010919 | 0.029583 | 0.20375 | 0.46924 | 0.69338 | 0.83682 | 0.91681 | 0.95842 | 0.97933 | 0.9897 | 0.99483 | 0.99737 | 0.99865 | 0.9993 | 0.99963 | 0.9998 | 0.99989 | 0.99994 | 0.99997 | 0.99998 | 0.99999 | 0.99999 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
RC_non-eng | 0 | 0.00014241 | 0.0054531 | 0.027929 | 0.071782 | 0.13264 | 0.20352 | 0.27818 | 0.35212 | 0.42247 | 0.48766 | 0.54696 | 0.60023 | 0.64766 | 0.68963 | 0.72661 | 0.75911 | 0.78761 | 0.81259 | 0.83446 | 0.85362 | 0.87041 | 0.88513 | 0.89804 | 0.90939 | 0.91936 | 0.92814 | 0.93587 | 0.9427 | 0.94873 | 0.95407 | 0.9588 | 0.96299 | 0.96671 | 0.97003 | 0.97298 | 0.97561 | 0.97796 | 0.98006 | 0.98194 | 0.98363
Timber / Bamboo | 0 | 2.1055e-06 | 0.0002177 | 0.0019626 | 0.0074541 | 0.018492 | 0.035847 | 0.059356 | 0.088258 | 0.1215 | 0.15796 | 0.19656 | 0.23637 | 0.27661 | 0.31662 | 0.35593 | 0.39415 | 0.43102 | 0.46634 | 0.5 | 0.53194 | 0.56213 | 0.59059 | 0.61735 | 0.64245 | 0.66597 | 0.68796 | 0.70852 | 0.7277 | 0.7456 | 0.76229 | 0.77784 | 0.79233 | 0.80582 | 0.81839 | 0.8301 | 0.841 | 0.85115 | 0.86061 | 0.86941 | 0.87762
GoN 2011 Census
GoN 2011 Census
HAZUS & Emily So
GEM & NSET
Earthquake Loss Modelling
Population and building data from 2011 National Census
Fragility curves and fatality rates from global empirical data (Guragain, 2012; HAZUS, GEMECD)
Verified on the 2015 earthquake
30 EQs for 3 different times = 90 scenarios
Building Typology | Fatality Rate
Adobe | 5.0%
Bamboo | 0.5%
Timber | 2.0%
Reinforced Concrete | 10.0%
Brick with flexible flooring | 5.0%
Brick with rigid flooring | 15.0%
Brick in mud mortar | 5.0%
Stone in mud mortar | 5.0%

## Slide 4
Scenario Ensembles
Scenario (Location-Fault_Mag) | Time of Day |  | 
 | Work Day | Non-work Day | Night
Wind-MFT_8.6 | 10,631 | 16,023 | 24,137
FWMW-MFT_8.6 | 36,770 | 53,175 | 81,434
WC-MFT_8.6 | 74,256 | 85,299 | 144,394
CE-MFT_8.6 | 65,946 | 71,960 | 124,942
Eind-MFT_8.6 | 15,231 | 20,321 | 32,665
W-Ind-MFT_8.3 | 5,908 | 8,956 | 13,458
FW-MFT_8.3 | 15,907 | 24,490 | 36,544
MW-MFT_8.3 | 24,404 | 37,559 | 56,089
W-MFT_8.3 | 32,200 | 43,013 | 68,178
C-MFT_8.3 | 53,025 | 55,444 | 98,375
E-MFT_8.3 | 23,731 | 30,196 | 49,265
Eind-MFT_8.3 | 7,536 | 10,608 | 16,679
WInd-MFT_7.8 | 3,100 | 5,070 | 7,429
FW-MFT_7.8 | 8,561 | 14,070 | 20,491
MW-MFT_7.8 | 12,796 | 21,050 | 30,638
W-MFT_7.8 | 19,644 | 26,476 | 41,891
C-MFT_7.8 | 38,333 | 36,876 | 68,301
E-MFT_7.8 | 9,739 | 14,316 | 22,200
Eind-MFT_7.8 | 3,791 | 5,911 | 8,902
WInd-MFT_7.0 | 856 | 1,298 | 1,958
FW-MFT_7.0 | 6,474 | 10,338 | 15,259
MW-MFT_7.0 | 8,518 | 13,645 | 20,090
W-MFT_7.0 | 11,369 | 16,400 | 25,114
C-MFT_7.0 | 28,038 | 23,261 | 46,414
E-MFT_7.0 | 6,882 | 9,916 | 15,537
Eind-MFT_7.0 | 2,267 | 3,372 | 5,134
SChn-KKM_7.8 | 166 | 323 | 523
MW-WFSN_7.8 | 5,292 | 9,023 | 13,042
MW-WFSS_7.3 | 7,361 | 12,134 | 17,727
W-TKG_7.3 | 1,560 | 2,531 | 3,798
Average | 18,010 | 22,768 | 37,020

## Slide 5
Scenario Results
Chart: Distribution of modelled earthquake fatalities in Nepal
| 5000 | 10000 | 15000 | 20000 | 25000 | 30000 | 35000 | 40000 | 45000 | 50000 | 55000 | 60000 | 65000 | 70000 | 75000 | 80000 | 85000 | 90000 | 95000 | 100000 | 105000 | 110000 | 115000 | 120000 | 125000 | 130000 | 135000 | 140000 | 145000 | 150000
 | 13 | 17 | 11 | 9 | 10 | 3 | 4 | 5 | 2 | 2 | 2 | 2 | 0 | 3 | 2 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
Cumulative | 13 | 30 | 41 | 50 | 60 | 63 | 67 | 72 | 74 | 76 | 78 | 80 | 80 | 83 | 85 | 85 | 86 | 87 | 87 | 88 | 88 | 88 | 88 | 88 | 89 | 89 | 89 | 89 | 90 | 90
Worst-case - 144,394
Average (median) – 25,932
Most common – 5,00010,000
Variability – 0.180

## Slide 6
Variability
0.00
0.33
0.66
1.00
Impacts are consistent and typically near to the minimum
Impacts are different in every different scenario
Impacts are consistent and typically near to the maximum
Plan for the AVERAGE because we know the worst-case is very unlikely
Plan for the WORST-CASE because we don’t know what impacts will occur
(precautionary approach)
Plan for the WORST-CASE because we know the worst-case is very likely
Zone of discretion?
0.30
0.36

## Slide 7
Province 1
Fatalities:
Likelihood: 43%
Average: 5,500
Worst-case: 20,000 Variability: 0.329 - Avg
Injuries:
Likelihood: 64%
Average: 18,000
Worst-case: 138,000
Variability: 0.295 - Avg
Building Damage:
Likelihood: 50%
Average: 24,000
Worst-case: 79,000 Variability: 0.423 - Max

## Slide 8
Province 2
Fatalities:
Likelihood: 59%
Average: 800
Worst-case: 17,000 Variability: 0.176 - Avg
Injuries:
Likelihood: 89%
Average: 3,000
Worst-case: 89,000
Variability: 0.165 - Avg
Building Damage:
Likelihood: 70%
Average: 3,000
Worst-case: 39,000 Variability: 0.231 - Avg

## Slide 9
Province 3
Fatalities:
Likelihood: 72%
Average: 3,000
Worst-case: 58,000 Variability: 0.205 - Avg
Injuries:
Likelihood: 92%
Average: 10,000
Worst-case: 274,000
Variability: 0.217 - Avg
Building Damage:
Likelihood: 77%
Average: 11,000
Worst-case: 172,000 Variability: 0.289 - Avg

## Slide 10
Province 4
Fatalities:
Likelihood: 84%
Average: 1,400
Worst-case: 20,000 Variability: 0.222 - Avg
Injuries:
Likelihood: 97%
Average: 8,000
Worst-case: 122,000
Variability: 0.249 - Avg
Building Damage:
Likelihood: 87%
Average: 11,000
Worst-case: 79,000 Variability: 0.319 - Avg

## Slide 11
Province 5
Fatalities:
Likelihood: 77%
Average: 4,500
Worst-case: 35,000 Variability: 0.218 - Avg
Injuries:
Likelihood: 96%
Average: 25,000
Worst-case: 202,000
Variability: 0.236 - Avg
Building Damage:
Likelihood: 87%
Average: 17,000
Worst-case: 107,000 Variability: 0.308 – Avg
* Worst-case in hills – 44,000
* Average in terai – 3,000

## Slide 12
Province 6
Fatalities:
Likelihood: 64%
Average: 2,200
Worst-case: 11,000 Variability: 0.288 - Avg
Injuries:
Likelihood: 82%
Average: 11,000
Worst-case: 84,000
Variability: 0.278 - Avg
Building Damage:
Likelihood: 70%
Average: 10,000
Worst-case: 42,000 Variability: 0.388 - Max

## Slide 13
Province 7
Fatalities:
Likelihood: 61%
Average: 2,000
Worst-case: 17,000 Variability: 0.250 - Avg
Injuries:
Likelihood: 80%
Average: 6,000
Worst-case: 109,000
Variability: 0.253 - Avg
Building Damage:
Likelihood: 63%
Average: 10,000
Worst-case: 53,000 Variability: 0.376 - Max

## Slide 14: Thank you!